## Slide 1: Module 9: Address Resolution
Introduction to Networks v7.0 (ITN)
Notes: Cisco Networking Academy Program
Introduction to Networks v7.0 (ITN)
Module 9: Address Resolution

## Slide 2: Module Objectives
Module Title: Address Resolution
Module Objective: Explain how ARP and ND enable communication on a network.
Topic Title | Topic Objective
MAC and IP | Compare the roles of the MAC address and the IP address.
ARP | Describe the purpose of ARP.
Neighbor Discovery | Describe the operation of IPv6 neighbor discovery.
Notes: 2
9 - Address Resolution
9.0.2

## Slide 3: 9.1 MAC and IP

## Slide 4: MAC and IP Destination on Same Network
There are two primary addresses assigned to a device on an Ethernet LAN:
  Layer 2 physical address (the MAC address) – Used for NIC to NIC communications on the same Ethernet network.
  Layer 3 logical address (the IP address) – Used to send the packet from the source device to the destination device.
  Layer 2 addresses are used to deliver frames from one NIC to another NIC on the same network. If a destination IP address is on the same network, the destination MAC address will be that of the destination device.

## Slide 5: MAC and IP Destination on Remote Network
When the destination IP address is on a remote network, the destination MAC address is that of the default gateway.
  ARP is used by IPv4 to associate the IPv4 address of a device with the MAC address of the device NIC.
  ICMPv6 is used by IPv6 to associate the IPv6 address of a device with the MAC address of the device NIC.

## Slide 6: 9.2 ARP
Notes: 9 - Address Resolution
9.2 ARP

## Slide 7: ARP ARP Overview
A device uses ARP to determine the destination MAC address of a local device when it knows its IPv4 address.
ARP provides two basic functions:
  Resolving IPv4 addresses to MAC addresses
  Maintaining an ARP table of IPv4 to MAC address mappings

## Slide 8: ARP ARP Functions
To send a frame, a device will search its ARP table for a destination IPv4 address and a corresponding MAC address.
  If the packet’s destination IPv4 address is on the same network, the device will search the ARP table for the destination IPv4 address.
  If the destination IPv4 address is on a different network, the device will search the ARP table for the IPv4 address of the default gateway.
  If the device locates the IPv4 address, its corresponding MAC address is used as the destination MAC address in the frame.
  If there is no ARP table entry is found, then the device sends an ARP request.

## Slide 9: ARP Removing Entries from an ARP Table
Entries in the ARP table are not permanent and are removed when an ARP cache timer expires after a specified period of time.
The duration of the ARP cache timer differs depending on the operating system.
ARP table entries can also be removed manually by the administrator.

## Slide 10: ARP ARP Tables on Networking Devices
The show ip arp command displays the ARP table on a Cisco router.
The arp –a command displays the ARP table on a Windows 10 PC.
R1# show ip arp
Protocol Address Age (min) Hardware Addr Type Interface
Internet 192.168.10.1 - a0e0.af0d.e140 ARPA GigabitEthernet0/0/0
C:\Users\PC> arp -a
Interface: 192.168.1.124 --- 0x10
Internet Address Physical Address Type
192.168.1.1 c8-d7-19-cc-a0-86 dynamic
192.168.1.101 08-3e-0c-f5-f7-77 dynamic

## Slide 11: ARP ARP Issues – ARP Broadcasting and ARP Spoofing
ARP requests are received and processed by every device on the local network.
Excessive ARP broadcasts can cause some reduction in performance.
ARP replies can be spoofed by a threat actor to perform an ARP poisoning attack.
Enterprise level switches include mitigation techniques to protect against ARP attacks.

## Slide 12: 9.3 IPV6 Neighbor Discovery

## Slide 13: IPv6 Neighbor Discovery IPv6 Neighbor Discovery Messages
IPv6 Neighbor Discovery (ND) protocol provides:
  Address resolution
  Router discovery
  Redirection services
ICMPv6 Neighbor Solicitation (NS) and Neighbor Advertisement (NA) messages are used for device-to-device messaging such as address resolution.
ICMTPv6 Router Solicitation (RS) and Router Advertisement (RA) messages are used for messaging between devices and routers for router discovery.
ICMPv6 redirect messages are used by routers for better next-hop selection.

## Slide 14: IPv6 Neighbor Discovery IPv6 Neighbor Discovery – Address Resolution
IPv6 devices use ND to resolve the MAC address of a known IPv6 address.
ICMPv6 Neighbor Solicitation messages are sent using special Ethernet and IPv6 multicast addresses.

## Slide 15: 9.4 Module Practice and Quiz
Notes: 9 - Address Resolution
9.4 Module Practice and Quiz

## Slide 16: Module Practice and Quiz What did I learn in this module?
Layer 2 physical addresses (i.e., Ethernet MAC addresses) are used to deliver the data link frame with the encapsulated IP packet from one NIC to another NIC on the same network.
If the destination IP address is on the same network, the destination MAC address will be that of the destination device.
When the destination IP address (IPv4 or IPv6) is on a remote network, the destination MAC address will be the address of the host default gateway (i.e., the router interface).
An IPv4 device uses ARP to determine the destination MAC address of a local device when it knows its IPv4 address.
ARP provides two basic functions: resolving IPv4 addresses to MAC addresses and maintaining a table of IPv4 to MAC address mappings.
After the ARP reply is received, the device will add the IPv4 address and the corresponding MAC address to its ARP table.
For each device, an ARP cache timer removes ARP entries that have not been used for a specified period of time.
IPv6 does not use ARP, it uses the ND protocol to resolve MAC addresses.
An IPv6 device uses ICMPv6 Neighbor Discovery to determine the destination MAC address of a local device when it knows its IPv6 address.
Notes: 9 – Address Resolution
9.4 – Module Practice and Quiz
9.4.1 – What did I learn in this module?
9.4.2 – Module Quiz – Address Resolution

## Slide 17: Module 9: Address Resolution New Terms and Commands
Address Resolution Protocol (ARP) ARP table show ip arp arpr -a ICMPv6 Neighbor Discovery protocol (ND) ICMPv6 Neighbor Solicitation (NS) message ICMPv6 Neighbor Advertisement (NA) message ICMPv6 Router Solicitation (RS) message ICMPv6 Router Advertisement (RA) message ICMPv6 Redirect Message |